## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – 26166
Problem Statement Title – Multi-modal, Sun angle and scale invariant image correspondence using Chandrayaan-2 optical images (OHRC, TMC and IIRS)
Theme – Space Technology
PS Category – Software
Team ID – To be added once allotted on the SIH portal
Team Name (Registered on portal) – Shevolution

## Slide 2: IDEA TITLE
Proposed Solution (Describe your Idea/Solution/Prototype)
Detailed explanation: geo.align_pair scale-normalizes CH2 OHRC vs LRO NAC onto one grid; SIFT, a custom mod-π illumination-invariant descriptor, and LightGlue are then benchmarked on the same ground truth.
How it addresses the problem: sun-angle change collapses SIFT (inliers ~1580 → single digits by 30°); LightGlue holds 80–94% grid coverage through 60°+ of sun-angle difference where classical descriptors fail.
Innovation: fit_reliability auto-flags registrations whose inliers reduce to ≤4 unique points as untrustworthy; results export natively as an ISIS PVL control network for ISRO's jigsaw pipeline.
Shevolution

## Slide 3: TECHNICAL APPROACH
Technologies: Python, OpenCV, NumPy/SciPy, Shapely, PyTorch (LightGlue + SuperPoint), rasterio, pdr (PDS3/4), webgeocalc (NAIF SPICE), pvl (ISIS control-net); 188 automated pytest cases.
Methodology: Product (CH2 OHRC | LRO NAC) → align_pair (common-grid resample) → prep (contrast-norm, mod-π orientation) → match/match_tiled (SIFT | mod-π | LightGlue, MAGSAC, sub-pixel) → metrics (RMSE, coverage, fit_reliability) → deliverable + ISIS control network.
Shevolution

## Slide 4: FEASIBILITY AND VIABILITY
Feasibility: 188/188 automated tests pass on hand-checkable synthetic ground truth; real PDS3/PDS4 parsing and NAIF SPICE geometry confirmed end-to-end on genuine CH2/LRO data, all open-source.
Challenges and risks: on a real CH2×LRO pair (~26.5% overlap), align_pair's single 4-corner perspective fit drifts along a long, narrow, curved-orbit strip — no trustworthy registration there yet.
Strategy: a multi-control-point / piecewise geometric model for align_pair is the scoped next step; fit_reliability surfaces this limitation honestly instead of a false win.
Shevolution

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience: cuts manual tie-point selection effort in ISRO's photogrammetry pipeline for sun-angle-mismatched pairs otherwise discarded as unusable.
Benefits: cross-mission data fusion (Chandrayaan-2 × LRO) despite differing instruments/illumination; self-verified output means no silent false positives; extensible to any georeferenced planetary matching problem.
Shevolution

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
mod-π's basis: RIFT, HAPCG illumination-robust remote-sensing matching literature.
LightGlue / SuperPoint — strongest benchmarked matcher in this project's own testing.
USGS ISIS control-network (PVL) format — validated via the independent pvl parser.
PDS3 (LRO) / PDS4 (Chandrayaan-2) label specs — source formats read natively.
NAIF SPICE / WebGeocalc — real solar-geometry (incidence, subsolar azimuth) for LRO.
Shevolution